Performance and Sludge Characteristics of UASB reactor Treated Low Concentration Domestic Wastewater at Psychrophilic Temperature

LUO Xiangnan1,2, JI Min1, YANG Jingliang2, ZHANG Jing2

(1. Department of Environmental Science and Engineering, Tianjin University, Tianjin, 300072;

2. Department of Environmental Science and Engineering, Hebei University of Science and Technology, Shijiazhuang, 050018)

Abstract：The performance and the sludge characteristics of an upflow anaerobic sludge blanket (UASB) reactor were investigated for the treatment of low concentration (COD 400-600mg.L-1) domestic wastewater at psychrophilic temperature (15±1℃). The laboratory-scale UASB reactor of 2.0L of useful volume was operated for a period of 174 days. An organic loading rate of around 3.0kg COD m-3d-1 was treated with a 30~50% COD removal rate. The characteristics of sludge in UASB reactor were changed. Granular sludge has been obtained in the reactor and was well settelable. The SEM photoes of the sludge during the experiment showed that filamentous bacterium and bacillus were key organisms. The ratio of polysaccharide and protein in extracellular polymeric substance (EPS) from sludge has close relative with the sludge granulation.

Key words： UASB reactor；psychrophilic temperature (15±1℃)；low concentration domestic wastewater；sludge characteristics；EPS

CLC number：X703       Document code：A

1 Introduction

Anaerobic treatment of wastewater is a technique with recycling use of energy at low cost. Technique of anaerobic treatment has its expansively developmental trend in the field of water pollution control as it accords with the situation of our country. Generally, Modern high-tate anaerobic reactors are typically applied to the treatment of high-strength wastewaters (COD>1000mg.L-1) in the mesophilic temperature range (25 to 40℃). But domestic wastewaters have typically concentration of COD below 1000mg.L-1 and many wastewaters have temperatures lower than mesophilic range (<25℃). Successful anaerobic treatment of such wastewaters with low cost and energy requirements would have an important influence on wastewater treatment [1]. Several authors studied and observed some successful results in recent years [2,3,4,5,6,7]. This experiment did elementary study on treatment of low concentration domestic wastewater by using UASB reactor at psychrophilic temperature (15±1℃) to supply anaerobic technique applied in northern regions at low temperature with design foundations and technical support.

2 Materials and methods

2.1 Experimental set-up

The laboratory-scale UASB reactor was made of organic glass (volume, height, diameter: 2.0L, 74cm, 5.2cm). The temperature of the reactor’s contents was controlled at (15±1) ℃ by a biochemical incubator. The Experimental system is shown in Fig. 1

Fig.1 Schematic diagram of the experimental system

基金项目：河北省科技厅基金资助项目（04276704），河北省建设厅基金资助项目（2005-125）

作者简介：罗湘南（1971年生），女，河北科技大学副教授，天津大学在读博士；Email：luoxiangnan@263.net

2.2 Experimental wastewater

Experimental wastewater is the artificial prepared organic wastewater with low concentration, in which glucose was used as carbon source and trace element necessary for the growth of microorganism was properly put. The compositions of experiment wastewater wastewater are showned in Table 1, and the compositions of of trace element solution are showned in Table 2.

Table 1 Compositions of experiment wastewater

| Component | Glucose | (NH4)2CO3 | KH2PO4 | NH4Cl | CaCl2 | MgSO4 | Na2CO3 | Yeast leaching solution |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Concentration(g.L-1) | 0.5 | 0.01 | 0.01 | 0.01 | 0.001 | 0.002 | 0.1 | 0.2 |

Table 2 Compositions of trace element solution

| Component | Concentration(g.L-1) | Component | Concentration(g.L-1) |
| --- | --- | --- | --- |
| FeCl3·4H2O | 0.08 | (NH4)6Mo7O24·4H2O | 0.004 |
| MnCl2·4H2O | 0.02 | CoCl2·6 H2O | 0.08 |
| NiCl2·6H2O | 0.002 | ZnCl2 | 0.002 |
| EDTA | 0.04 | CuCl2·2H2O | 0.0012 |

2.3 Seed sludge

Seed sludge was obtained from the digested pool of western bridge sewage disposal plant of Shijiazhuang. Sludge presented floccular and black, with SS of 90.33g.L-1 and VSS of 44.45g.L-1.

2.4 Analytical methods

During the experiment, pH, chamical oxygen demond (COD), suspended solids (SS), volatile suspended solids (VSS), volatile fatty acids (VFA), polysaccharide and protein analysis were carried out using the Standard Methods of China.

3. Results and discussion

3.1 Operation of UASB reactor

The UASB reactor was inoculated with mesophilic anaerobic sludge. The organic loading rate (OLR) in the start-up stage was 0.5kgCODm-3d-1.In the OLR rising stage, the OLR was raised for three times at 0.5kgCODm-3d-1.The highest OLR was 2.0kgCOD m-3d-1.In the third stage, OLR was raised for two times from 2.0kgCOD m-3d-1 to 3.0kgCOD m-3d-1. COD removal rate was aboved 30~50%. As shown in Fig. 2, a full and stable conversion capacity of psychrophilic UASB system can be achieved within 174 days.

# Fig.2 Operation results of the UASB reactor for treating low concentration wastewater at (15±1) ℃.

# (▲)removal rate(■) OLR

3.2 sludge characteristics

Duing the course of the experiment, seed sludge became floccular with good settling characteristic and at last became granular sludge. Characteristics of the sludge were observed by SEM as shown in Fig 3. The SEM photoes of the granular sludge showed that filamentous bacterium and bacillus were key organisms. The long-term operation performance of the UASB reactor system reveals thr satisfactory development the activity of the filamentous bacterium and bacillus in sludge.

Fig.3 SEM of the microbios in sludge (a) the start-up stage

(b) the OLR rising stage (c) the granulating stage

3.3 EPS in sludge

Extracellular polymeric substances (EPS) of the sludge in the reactor play an important role in sludge granulation. The main compoents of EPS are polysaccharide and protein. The isolated EPS was investigated.The ratio of polysaccharide and protein is shown in Fig. 4. It was showed that EPS has close relative with the sludge granulation.The lower the ratio of polysaccharide and protein was, the higher the stabilization of the granular sludge was.

Fig.4 Ratio of polysaccharide and protein of EPS

4 Conclusions

Form the results obtained, the following conclusions can be drawn:

The upflow anaerobic sludge blanket (UASB) reactor presented a stable operation and high performance in the treatment of low concentration (COD 400-600mg.L-1) domestic wastewater at psychrophilic temperature (15±1℃). At psychrophilic temperature, the observed increased activity of filamentous bacterium and bacillus could be due to granularation of sludge. EPS can also play an important role in maintaining the stability of granules.

References:

[1] Gatze Lettinga, Salih Rebac, Grietje Zeeman. Challenge of psychrophilic anaerobic wastewater treatment [J]. Trends in Biotechnology, 2001, 19(9):363-370

[2] Tarek A. Elmitwalli, Marcel H. Zandvoort, Grietje Zeeman, et al. Low temperature treatment of domestic sewage in upflow anaerobic sludge blanket and anaerabic hybrid reactors [J]. Water Science and Technology, 1999, 39(5):177-185

[3] Tarek A. Elmitwalli, Kim L.T.Oahn, Grietje Zeeman, et al. Treatment of domestic sewage in a two-step anaerobic filter/anaerobic hybrid system at low temperature [J]. Water Reasearch, 2002, 36:2225-2232

[4] Salih Rebac, Jules B. van Lier, Piet Lens, et al. Psychrophilic anaerobic treatment of low strength wastewaters [J]. Water Science and Technology, 1999, 39(5):203-210

[5] Alette A.M. Langenhoff, David C.Stuckey. Treatment of dilute wastewater using an anaerobnic baffled reactor: effect of low temperature [J]. Water Reasearch, 2000, 35(15):3867-3875

[6] Gatze Lettinga, Salih Rebac,Sofia Parshina, et al. High-Rate anaerobic treatment of wastewater at low temperatures [J]. Applied and Environmental Microbiology, 1999, 65(4):1696-1702

[7] Nidal Mahmoud, Grietje Zeeman, Huub Gijzen, Anaerobic sewage treatment in one-stage UASB reactor and combined UASB-digestor system. [J]. Water Reasearch, 2004, 38: 2347~2357

UASB反应器处理低温低浓度污水工作状况及污泥特性

罗湘南1,2，季民1，杨景亮2，张静2

(1.天津大学环境科学与工程学院，天津 300072；

2.河北科技大学环境科学与工程学院，石家庄 050018)

摘  要: 采用有效容积为2.0L的低温（15±1℃）上流式厌氧污泥床反应器，以厌氧消化污泥作为接种物，处理COD为400～600mg/L的葡萄糖模拟生活污水，考察了反应器的工作状况及污泥特性，获得了控制条件对促进微生物固定化的影响规律。试验历时174个运行日。反应器最高容积负荷达到3.0kgCODm-3d-1，COD去除率为30~50%。在试验运行过程中，反应器内的污泥实现了颗粒化,，且沉降性能稳定良好。扫描电镜照片显示，污泥中丝状菌和杆状菌是颗粒污泥中微生物组成的优势种群。测试结果表明：颗粒污泥胞外多聚物（EPS）中多糖与蛋白质的比值与颗粒污泥的形成紧密相关。

关键词：UASB反应器；低温（15±1℃）；低浓度生活污水；污泥特性；胞外多聚物（EPS）

中图分类号：X703    文献标识码：A

# Text boxes

1-Upflow Anaerobic Sludge Bed reactor; 2-recirculating pump; 3- water inlet pump; 4-collecting trough   5-water outlet;

6-water seal 7-gas flowmeter; 8-gas effluent

b

a

c